## Slide 1
Distillation for flavour
Richard Archer

## Slide 2
Thank you for inviting me
Logan Campbell Professor Food Technology – Massey University
Before that 20 years in Dairy Industry
Before that, 5 years fermentation and deer by-products industries

## Slide 3
Water - it sticks TO ITSELF

## Slide 4
Water - and wriggles

## Slide 5
changes with temperature
Higher temperature:
  More wriggling
  Tears some H-bonds apart
At room temp, liquid water in gangs of three
At higher temps in gangs or two or as loners
At lower temps in bigger and bigger clumps

## Slide 6
changes with temperature
Tearing apart takes energy
Specific heat capacity
To heat 1 kg of water by 1°C takes 4.18 kJ
  Or 0.0012 kWh
  Or 0.03 cents

## Slide 7
changes with temperature
Tearing apart takes energy
To heat 1 kg of water by 1°C takes 4.18 kJ
To heat 1 kg of copper by 1°C takes only 0.38 kJ

## Slide 8
changes with temperature
Tearing apart takes energy
To heat 1 kg of water by 1°C takes 4.18 kJ
To heat 1 kg of copper by 1°C takes only 0.38 kJ
To heat 1 kg of ethanol by 1°C takes 2.46 kJ

## Slide 9
changes with temperature
Below zero water is solid ice
Above 100 °C water is gas (for 1 atmosphere pressure)

## Slide 10
changes with temperature
For 1 kg water to melt from ice to water at 0°C:
  Takes 334 kJ of energy
  Enough to heat that 1kg of water from 0°C to 80°C
For 1 kg water to evaporate at 100°C:
  Takes 2260 kJ of energy
  Enough to heat 1kg of water from 0°C to 542°C !!

## Slide 11
changes with temperature
For 1 kg water to melt from ice to water at 0°C:
  Takes 334 kJ of energy
  Enough to heat that 1kg from 0°C to 80°C
  Or 0.09 kWh or ~2.3 cents
For 1 kg water to evaporate at 100°C:
  Takes 2260 kJ of energy
  Enough to heat 1kg from 0°C to 542°C
  Or 0.63 kWh or ~ 16 cents

## Slide 12
changes with temperature
For 1 kg water to evaporate at 100°C:
  Takes 2260 kJ of energy
  Or 0.63 kWh or ~ 16 cents
For 1 kg ethanol to evaporate at 78 °C:
  Takes 850 kJ of energy
  Or ~6 cents

## Slide 13
Vapour pressure
Liquid water always gives off some water vapour
  At 0°C zero degrees vapour pressure is 0.6 kPa
  At 80°C it is 46 kPa
  At 100 °C is 101 kPa = one atmosphere

## Slide 14
Vapour pressure
25°C
50°C
100°C
78.4°C
19 kPa
Water
3 kPa
Water
43 kPa
Water
101 kPa
Water
Liquid water always gives off some water vapour

## Slide 15
Vapour pressure
25°C
50°C
100°C
78.4°C
19 kPa
Water
3 kPa
Water
43 kPa
Water
101 kPa
Water
Ethanol
8 kPa
Ethanol
Ethanol
Ethanol
46 kPa
101 kPa

## Slide 16
Water Ethanol beta-pinene
Ethanol quite likes water – hydrophilic – fully miscible
Βeta-pinene hates water – hydrophobic – immiscible
Beta-pines likes ethanol - soluble

## Slide 17
alpha-pinene
Melts at -63 °C so likes to be liquid normally
Βoils at 157 °C so hard to get it into vapour

## Slide 18
alpha-pinene
Melts at -63 °C so likes to be liquid normally
Βoils at 157 °C so hard to get it into vapour
Unless you put it into water-ethanol which it doesn’t like

## Slide 19
Major gin cogeners - hydrophobic
Beta-pinene boils ~166 °C
Limonene boils ~176 °C
Citronellal boils ~204 °C
Terpinene boils at ~174 °C
  And melts at 60 °C – usually solid

## Slide 20
VOLATILITY of Cogeners in Aq-ETOH
Absolute volatility of X =
  When the mix is boiling
[mole fraction = fraction of # of molecules]
Chart: Mole fraction EtOH for ABV value
| 100 | 99 | 98 | 97 | 96 | 95 | 94 | 93 | 92 | 91 | 90 | 88 | 86 | 84 | 82 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15 | 10 | 5 | 0
 | 1 | 0.96849 | 0.93831 | 0.9094 | 0.88166 | 0.85503 | 0.82945 | 0.80485 | 0.78117 | 0.75838 | 0.73641 | 0.69479 | 0.65599 | 0.61973 | 0.58577 | 0.55391 | 0.4822 | 0.42006 | 0.36568 | 0.3177 | 0.27505 | 0.23689 | 0.20254 | 0.17146 | 0.14321 | 0.11742 | 0.093771 | 0.072017 | 0.051935 | 0.033341 | 0.016075 | 0
vapour
liquid

## Slide 21
VOLATILITY of gin Cogeners in Aq-ETOH
Esteban-Decloux et al J. Inst. Brew. 2022 128:171-187

## Slide 22
VOLATILITY of ALDEHYDES in Aq-ETOH
Esteban-Decloux et al J. Inst. Brew. 2022 128:171-187
Notes: Pentanal – quite hydrophilic – happier to stay in boiling water than others

## Slide 23
VOLATILITY of ESTERS in Aq-ETOH
Esteban-Decloux et al J. Inst. Brew. 2022 128:171-187

## Slide 24
VOLATILITY of VF Acids in Aq-ETOH
Esteban-Decloux et al J. Inst. Brew. 2022 128:171-187

## Slide 25
Gin
Ester
Aldehydes
Acids
Esteban-Decloux et al J. Inst. Brew. 2022 128:171-187

## Slide 26
Whisky Batch Distillation
Wash – foreshots – includes methanol – chuck
Spirit – heads – smaller aldehydes etc
Next – middle cut – esters, good flavours product
Next – late middle cut – smoke phenolics product
Finally – tails – hydrophobic, high boiling acids, aldehydes

## Slide 27
WHAT happens to the Rubbish?
Acids that get recycled to the next batch?
Aldehydes that get recycled?
What happens when they are redistilled in another batch? Same?

## Slide 28
WHAT happens to the Rubbish?
Acids that get recycled to the next batch?
Aldehydes that get recycled?
What happens when they are redistilled in another batch? Same?
Do they “break down” and disappear?
They must shape-shift to make the middle cut next time round….

## Slide 29
WHAT happens to the Rubbish?
Aldehydes can oxidise to organic acids….
Organic acids can react with ethanol to form esters….
Organic acids
Ethanol
Esters
?

## Slide 30
the Rubbish turns to gold?
Early in a batch still run ethanol in the vapours in high (water low)
Further up the lyne arm ethanol in vapours higher
Inside of beaten copper vessels get flaky as they age
Just the conditions for esterification??
Organic acids
Ethanol
Esters
Up here!

## Slide 31
Energy needs of distillation
Water needs 2260 kJ for 1 kg
Ethanol needs 850 kJ for 1 kg
Energy demand climbs during a run:
Constant heat  declining evaporation rate
Chart: Latent Heat of EtOH/Water
| 100 | 99 | 98 | 97 | 96 | 95 | 94 | 93 | 92 | 91 | 90 | 88 | 86 | 84 | 82 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15 | 10 | 5 | 0
 | 850 | 867.7277 | 885.3634 | 902.908 | 920.3621 | 937.7264 | 955.0016 | 972.1884 | 989.2875 | 1006.2995 | 1023.2251 | 1056.8197 | 1090.0765 | 1123.0005 | 1155.5968 | 1187.8702 | 1267.1721 | 1344.5575 | 1420.0951 | 1493.8503 | 1565.8854 | 1636.26 | 1705.0307 | 1772.2518 | 1837.9751 | 1902.25 | 1965.124 | 2026.6424 | 2086.8485 | 2145.7839 | 2203.4883 | 2260

## Slide 32
Energy needs of distillation
Water needs 2260 kJ for 1 kg
Ethanol needs 850 kJ for 1 kg
Energy demand climbs during a run:
Constant heat  declining evaporation rate
Chart: Latent Heat of EtOH/Water
| 100 | 99 | 98 | 97 | 96 | 95 | 94 | 93 | 92 | 91 | 90 | 88 | 86 | 84 | 82 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 15 | 10 | 5 | 0
 | 850 | 867.7277 | 885.3634 | 902.908 | 920.3621 | 937.7264 | 955.0016 | 972.1884 | 989.2875 | 1006.2995 | 1023.2251 | 1056.8197 | 1090.0765 | 1123.0005 | 1155.5968 | 1187.8702 | 1267.1721 | 1344.5575 | 1420.0951 | 1493.8503 | 1565.8854 | 1636.26 | 1705.0307 | 1772.2518 | 1837.9751 | 1902.25 | 1965.124 | 2026.6424 | 2086.8485 | 2145.7839 | 2203.4883 | 2260
~14 c/kg
~10 c/kg

## Slide 33
Energy needs of distillation
Still contents get wetter over run
Boiling point climbs
Constant heat  declining evaporation rate
  Temp driving force declines
  Unless you lift hot oil temp to compensate
Chart: Temperatures During Distillation Run
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110
Hot Oil | 105 | 105 | 105 | 105 | 105 | 105 | 105 | 105 | 105 | 105 | 105 | 105
Still contents | 83 | 84 | 85 | 85.9 | 86.9 | 87.9 | 88.8 | 89.8 | 90.7 | 91.6 | 92.5 | 93.3

## Slide 34
WHAT is reflux?
Think of three distillations runs in a row to get more and more pure
8%
40%
75%
92%

## Slide 35
WHAT is reflux?
But you need three lots of heating and cooling
8%
40%
75%
92%

## Slide 36
WHAT is reflux?
Unless:
  Use the heat over and over
  Bubbling through liquid
  Heat stronger spirit in next still
multiple distillations in one device
8%
92%

## Slide 37
Distillation column
8%
92%

## Slide 38
Distillation column

## Slide 39
Distillation column needs reflux
Need partial condensation of vapour
  To make liquid spirit
  To drain backward
  To condense upcoming vapours
  To act as multiple stages of still
  Selective condensation of high boiling stuff
Dephlegmator to condense only some of the vapours
Condenser + partial reflux
or

## Slide 40
When do you need a column?
If hard to get up to high alcohol
To knock down unwanted flavour components
To make clean neutral spirit of later use
  For gin making
  For blending

## Slide 41
A pot still has some reflux built in
Long/extended neck
Ball or lamp glass neck
Rising lyne arm

## Slide 42
A pot still and scale
Smaller still  more surface/volume
  More reflux
  More copper
  Different

## Slide 43
Gin - maceration
Soak some of the juniper in EtOH/water cold overnight
Solvent penetrates the juniper
  by diffusion
  by capillary action
Air bubbles likely to remain in pores and crevices

## Slide 44
Gin - maceration
Some osmosis across cell walls
Not much dissolving of target compounds – yet
  Very low solubility of target compounds in aqueous ethanol

## Slide 45
Gin - maceration
For some compounds botanical ratios makes a difference
γ-terpinene
350 mL 60% ABV
limonene
350 mL 60% ABV
11g juniper berry
5.8 g juniper berry
11g juniper berry
5.8 g juniper berry
From Beau Welch’s Master’s project
Notes: Higher ratios not always the best. Law of diminishing returns. Need to find an economic optimum berry:solvent ratio.

## Slide 46
Gin - maceration
Crushing berries before maceration helps extraction
β-myrcene
limonene
crushed berries
whole berries
vacuum
crushed berries
whole berries
vacuum
From Beau Welch’s Master’s project

## Slide 47
Gin - maceration
ABV affects extraction – higher appears slower
β-myrcene
limonene
96% ABV
80% ABV
60% ABV
80% ABV
96% ABV
60% ABV

## Slide 48
Gin - hydrodistillation
Boiling this mixture the next morning
Solubility climbs with temperature
But volatility very high
  Diffusion through solvent inside juniper
  Agitated by vigour of boil
  As soon as pinene (eg) reaches bubble wall it leaps into vapour
Juniper likely to act as bubble nucleation sites
  Careful if it goes off the boil and you restart…..may bump!

## Slide 49
Gin - hydrodistillation
90% of macerate extract reports to condensate when boiled
limonene
β-myrcene
α-pinene
distillate
macerate
raffinate
5.8 g
2.9 g
11.6 g
20 g in 350 mL
From Beau Welch’s Master’s project

## Slide 50
Gin – Botanicals basket
Many processes happening simultaneously
Vapour condensing heat botanicals to condensate boiling point
Wetting of botanicals with solvent
Dissolution, migration, evaporation of cogeners (good & bad)
Percolation through the bed and return to still – some leaching
Evaporation of cogener out of the EtOH/Water solution

## Slide 51
Gin – condensate percolation
α-pinene
Fraction 1
Fraction 2
Fraction 3
Fraction 5
Fraction 4
Fractions 1- 5 mixed
Full ratio of botanical:solvent
1/4 ratio
1/2 ratio
3/4 ratio
From Beau Welch’s Master’s project

## Slide 52
Gin – condensate percolation
γ-terpinene
β-myrcene
Fractions 1- 6 mixed
Fractions 1- 6 mixed
Mobile early
Mobile later
From Beau Welch’s Master’s project

## Slide 53
Gin – condensate percolation
citronellal
From Beau Welch’s Master’s project

## Slide 54
Gin – Botanicals basket
Start with high EtOH in the vapour
  Good for cogener solubility
  Bad for cogener volatility
As run proceeds vapours get wetter and hotter
Gin

## Slide 55
Gin – Botanicals basket
Temperature climbs as boiling/condensing point of vapours climbs
  Solvent in basket gets hotter
  Cogener solubility climbs a bit
Hydrophobic cogeners’ volatility climbs more
Gin

## Slide 56
Gin – Botanicals basket
Energy (latent heat) in the condensing vapour rises
May get some thermal breakdown of botanicals  vegetal notes
Gin

## Slide 57
Gin – Vapour distillation
limonene
γ-terpinene
β-myrcene
citronellal
Highest ratio not best
Highest ratio not best
From Beau Welch’s Master’s project

## Slide 58
summary
Basic physics of flavour distillation is well known
But spirit distillation is very complex
Lots of interactions between solvents, cogeners & botanicals
Science helps most in analysis of product

## Slide 59
summary
It is still an art-form
Partly because the product is art

## Slide 60
THANK you